## Slide 1
SRSI RESEARCH PROJECT
Occlusion-Adaptive Temporal Memory
A temporal video understanding framework for occlusion reasoning in autonomous vehicle perception
Noor Basfar
Notes: This follows straight after your hook - it's the reveal of what the project actually is. Introduce the project over the real dashcam frame: this is about helping self-driving car cameras keep track of road users even when something briefly blocks the view.

## Slide 2
THE PROBLEM IN AUTONOMOUS DRIVING
Single-Frame Detection Lacks Temporal Understanding
BEFORE
Car clearly visible
OCCLUDED
Fully hidden from view
AFTER
Reappears down the road
→
→
A detector that processes each frame in isolation cannot determine that the vehicle is still present during occlusion — it has no mechanism for reasoning across time.
“Like watching someone walk behind a parked bus — you don't assume they vanished.”
Target vehicle
Target hidden behind occluder
Target vehicle (reappeared)
Notes: Walk through this one real example frame by frame: the car is visible, then fully hidden behind other traffic, then reappears further down the road. Point out that most detectors process the middle frame in total isolation - to them, the car simply doesn't exist for that instant. That's the core problem this whole project is about.

## Slide 3
THE DATASET
nuScenes — Front Camera Only
1
nuScenes: a large-scale AV dataset with synchronized cameras, LiDAR, radar, and 3D box annotations that include a per-object visibility rating
2
This project uses only CAM_FRONT — one monocular camera, no LiDAR or other views feeding detection itself
3
Front-only keeps the pipeline laptop-scale and isolates the occlusion-memory problem, instead of mixing in multi-camera fusion
4
LiDAR and the 3D annotations aren't wasted, though — they come back as independent ground truth for evaluating OATM (next: Evaluation Methodology)
CAM_FRONT — the only view this project detects from
nuScenes sensor pipeline
Camera + LiDAR + Radar
CAM_FRONT selected
Detection input (YOLO)
→
→
Notes: Be upfront about scope before going further: this is nuScenes, and specifically only the forward-facing camera - no LiDAR, no side/rear cameras, no sensor fusion feeding the detector. That's a deliberate simplification to keep the study laptop-scale and focused purely on the occlusion-memory question. The payoff comes later - nuScenes' LiDAR and 3D annotations aren't part of detection, but they become the independent ground truth used to evaluate OATM, which is the next thing after the design slide.

## Slide 4
THE CORE RESEARCH QUESTION
Can temporal video understanding enable a camera to maintain reliable tracks of temporarily occluded road users, without introducing false detections?
Hypothesis
By incorporating temporal video understanding rather than relying on single-frame detection, occlusion-aware memory is expected to preserve more valid object tracks through short occlusions than conventional tracking methods, without producing an unacceptable number of false (ghost) tracks.
Notes: State the research question plainly and pause on it. This is the question the whole project is trying to answer, and the hypothesis is what we expect but haven't yet proven.

## Slide 5
METHODOLOGY
Manual Occlusion Staging
No automated tool identifies the precise moment an object becomes occluded or reappears. Each occlusion sequence in this study was therefore manually reviewed, frame by frame, and divided into five stages before any detector was run.
This manual staging is what makes the stage-by-stage detection results on the next slide meaningful — each stage boundary reflects a human judgment, not an automatic threshold.
1. No Occlusion
Target fully visible
→
2. First Partial
Occluder begins covering
→
3. Full Occlusion
Target entirely blocked
→
4. First Reappearance
Target partially visible
→
5. Full Appearance
Target fully visible again

## Slide 6
EVIDENCE 1 · BASELINE
Detection Performance Across Occlusion Stages
Pretrained YOLO nano, CPU-only, on 8 real nuScenes occlusion sequences — tracked through 5 stages, from clearly visible to fully hidden and back.
Chart: Detection rate by stage
| No Occlusion | First Partial Occlusion | Full Occlusion | First Partial Appearance | Full Appearance
Detection rate | 1 | 1 | 0.125 | 0.5 | 1
Chart: Mean confidence by stage (0 = undetected)
| No Occlusion | First Partial Occlusion | Full Occlusion | First Partial Appearance | Full Appearance
Mean confidence | 0.774 | 0.587 | 0.029 | 0.425 | 0.845
Full occlusion, sample_003: the detector produces no bounding box for the target. This reflects a missed detection, not a misclassification.
100% → 13%
detection rate at full occlusion
0.77 → 0.03
mean confidence at full occlusion
100%
correct class whenever detected
Partial-occlusion stages have small sample sizes (n=2-3) — interpret with caution.
Notes: Baseline setup: a plain, off-the-shelf YOLO detector, no memory at all. Point at the photo - that's the actual failure, a real frame where the detector produced zero boxes for the hidden target, not a simulated one. Detection rate stays perfect through partial occlusion then falls off a cliff at full occlusion. Confidence erodes before detection technically fails, and recovers once visible again.

## Slide 7
EVIDENCE 2 · NAIVE MEMORY
Baseline Approach: Static Position Retention
When the detector loses the target, its most recently observed bounding box is retained and continues to be displayed, rather than discarded.
BEST CASE
WORST CASE
sample_003 — reappears next to a bus (83 px, IoU 0.34 — boxes barely overlap by a third)
sample_006 — crossing an intersection (589 px, IoU 0.00)
Also tested: sample_001 (127px), sample_004 (423px), sample_005 (432px) — same pattern across all 5.
331 px
mean center error on reappearance
0.085
mean IoU (median: 0.000)
3 / 5
samples had zero box overlap
Notes: Introduce the naive fix: just freeze the last box while the target is hidden. Orange is the frozen memory box, green is the real detection once the object reappears. Best case they nearly line up; worst case the frozen box is nowhere near the real car. Not cherry-picked - all 5 valid samples follow the same pattern, mean error 331px, 3 of 5 with zero overlap at all.

## Slide 8
EVIDENCE 2 · NAIVE MEMORY
Static Position Retention: A Qualitative Comparison
Four views of the same sequence, shown side by side: the detector alone (track lost), static memory's retained position, motion-based prediction, and the withheld reference used to evaluate accuracy. The static-memory panel drifts away from the vehicle as it continues moving.
.

## Slide 9
EVIDENCE 3 · SORT MOTION PREDICTION
Motion-Based Prediction: Results and Limitations
A SORT-style tracker that predicts object velocity rather than retaining a fixed position, evaluated on 9 vehicle tracks.
Chart: Center error by gap length (px)
| 1 | 2 | 3 | 5 | 8 | 10
Static memory | 12.778 | 16.152 | 22.286 | 34.21 | 51.616 | 64.485
SORT motion | 3.472 | 3.3 | 4.588 | 6.503 | 14.295 | 31.329
Chart: Mean IoU by gap length
| 1 | 2 | 3 | 5 | 8 | 10
Static memory | 0.887 | 0.86 | 0.817 | 0.737 | 0.628 | 0.575
SORT motion | 0.921 | 0.905 | 0.882 | 0.838 | 0.702 | 0.57
46 → 17 px
mean center error, static → SORT
0.67 → 0.72
mean IoU, static → SORT
9 tracks
cars only, across 3 clips
THE CATCH
Most of the improvement is concentrated in 2 of the 9 tracks; on the dominant clip, static memory performs comparably to SORT. The reference boxes used for evaluation were Kalman-corrected rather than raw YOLO detections, and gaps exceeding the tracker's configured expiry threshold were not enforced. This demonstrates motion extrapolation under controlled conditions, not an independent validation of SORT.
Notes: Motion prediction beats a frozen box clearly - 46px down to 17px, IoU up from 0.673 to 0.720. But say the catch out loud: almost the whole win comes from 2 of 9 tracks, the reference boxes aren't fully independent, and long gaps bypass the tracker's own expiry rule. A real result, not yet a fully validated one.

## Slide 10
EVIDENCE 4 · BYTETRACK
Two-Stage Association for Low-Confidence Detections
Using the same evaluation setup as Evidence 3, ByteTrack performs a second association pass against low-confidence detections rather than discarding them immediately — evaluated on 12 natural weak-evidence events and 65 complete-absence frames, scored against projected nuScenes 3D ground truth.
58% → 67%
natural events recovered (SORT → ByteTrack)
33% → 50%
identity preserved through the event
2 → 0
false associations during complete detection absence
THE CATCH
The improvement is concentrated in the pedestrian class (2 of 4 events) and is drawn from only 5 target tracks across 4 scenes. It also applies only when a weak detection still exists; when the object is entirely undetected, ByteTrack relies on the same motion prediction as SORT.
This illustrates the distinction OATM's occlusion classifier is intended to model: weak-but-present evidence, where a secondary association step is beneficial, versus truly absent evidence, where only motion and uncertainty modeling can contribute.

## Slide 11
THE DIAGNOSIS
A static memory representation loses accuracy over time because it does not account for object motion.
Real objects continue moving while hidden. A memory system that retains only a past position becomes increasingly inaccurate the longer the object remains occluded.
THE GAP IN EXISTING TOOLS
Single-frame detection
Retains no information across frames; an occluded object is treated as absent
SORT
Reduces center error from 46 to 17 px on smooth trajectories; evaluated on 9 vehicle tracks with a circular reference
ByteTrack
Requires at least partial detection evidence to associate a track
Fixed temporal memory
Does not model motion and risks retaining tracks after the object has left the scene
None of these methods distinguish between an occluded, lost, or exited object, or adjust confidence accordingly — this is the gap OATM is designed to address.
Notes: This is the pivot of the whole talk. First state the diagnosis: naive memory fails because it ignores motion, and even real motion prediction (as just shown) only helps partially. Then name the gap in every existing lightweight method - none of them combine occlusion-causality reasoning, motion prediction, and confidence decay. That's the bridge into the OATM design on the next slide.

## Slide 12
PROPOSED APPROACH
OATM: Occlusion-Adaptive Temporal Memory
VISIBLE
OCCLUDED
LOST / EXITED
reappearance → back to VISIBLE
OATM
Appearance Memory
Last clear crop, for re-identification
Motion Memory
Kalman predict → observe → correct
Occlusion Classifier
VISIBLE / OCCLUDED / LOST / EXITED
Confidence Decay
Continuous decay; anti-ghost termination
Notes: Introduce OATM's core mechanism, and be specific about the motion half since that's the part judges will probe: it's not a vague promise, it's the same predict-observe-correct Kalman loop already built and tested in Evidence 3 - just corrected to use an independent reference box and to actually enforce track-expiry, the two flaws that experiment exposed. Appearance memory (last clear crop) handles re-identification; motion memory (position + velocity) handles where to look. The occlusion classifier decides how much to trust the motion prediction at any moment, and confidence decays smoothly rather than on a fixed timer. Be clear this is the proposed design - it has not been implemented or benchmarked yet, that's the next phase.

## Slide 13
EVALUATION METHODOLOGY
Ground Truth From LiDAR, Not the Camera Itself
LiDAR provides positional information independent of the camera, allowing OATM's predictions to be evaluated even when the target is not visible to the camera.
3D + LiDAR Ground Truth
nuScenes annotations, independent of camera
→
Project to CAM_FRONT
Standard transform chain into the camera view
→
Run OATM (Blind)
CAM_FRONT only, genuinely occluded
→
Score vs. Ground Truth
Never against another camera-based tracker
This ordering directly repairs the circularity in Evidence 3, where the reference boxes were derived from the same Kalman model being tested.
Notes: This is the answer to 'how will you actually know OATM is right.' The key move: ground truth comes from LiDAR and the 3D box annotations, not from another camera-derived tracker - so it isn't circular the way the SORT experiment's evaluation was. The front camera is blind during occlusion by design; LiDAR isn't, so it gives an independent check on whether OATM's predicted position is actually correct, not just self-consistent.

## Slide 14
SENSOR CONFIGURATIONS
Trade-offs in Perception System Design
A generic comparison of sensor configurations used in autonomous vehicle perception; OATM's row is a proposed capability, not yet implemented or measured.
Configuration | Description | Trade-off
Single camera | One forward-facing monocular camera | Lowest cost; occlusion causes complete information loss
LiDAR only | 360-degree point cloud, no camera imagery | Occlusion-robust geometry; no color or texture, higher cost
Multi-camera (5-6 cameras) | Full surround visual coverage | Redundant viewpoints reduce occlusion; higher compute and calibration cost
Camera + LiDAR fusion | Combines visual and geometric sensing | Most robust overall; highest cost and system complexity
Single camera + OATM (proposed) | Same low-cost hardware, with temporal occlusion reasoning added | Aims to approach fusion-level robustness without extra sensors; not yet benchmarked
Notes: Position OATM against the alternatives already used in the field. The point isn't that the others are bad - it's that none of them explicitly reason about *why* an object disappeared, which is what OATM adds. Reiterate that this row is a design claim to be tested, not a measured result.

## Slide 15
Roadmap
1. Test Sets
Natural + controlled occlusion sets from nuScenes
→
2. Fix Baselines
Repair SORT's circular reference; add ByteTrack
→
3. Metrics
Recall, identity, ghost-rate, recovery time
→
4. Data Splits
By scene, not frame, to avoid leakage
→
5. Extend Scope
From vehicles to pedestrians
Notes: Close with the roadmap: this baseline experiment was step one, the frozen-memory experiment was step two, the SORT test was step three. Next comes fixing the SORT experiment's methodology, building proper test sets, implementing OATM itself, and comparing it fairly against existing tracking methods. Also flag scope: everything so far has been vehicles - pedestrians and other vulnerable road users are the next class to extend to, since that's arguably the higher-stakes case. Open the floor for questions.

## Slide 16
References
Ma, J., Yang, J., Fu, F., Hao, D., & Wang, R. (2026). Occlusion-aware multi-camera 3D multi-object tracking with dual-appearance dynamic association. Applied Soft Computing.
Pang, Z., Li, J., Tokmakov, P., Chen, D., Zagoruyko, S., & Wang, Y.-X. (2023). Standing Between Past and Future: Spatio-Temporal Modeling for Multi-Camera 3D Multi-Object Tracking. CVPR 2023. arXiv:2302.03802.
Anwar, N., Bilodeau, G.-A., & Bouachir, W. (2024). STF: Spatio-Temporal Fusion Module for Improving Video Object Detection. arXiv:2402.10752.
Cai, J., Xu, M., Li, W., Xiong, Y., Xia, W., Tu, Z., & Soatto, S. (2022). MeMOT: Multi-Object Tracking with Memory. CVPR 2022, pp. 8080-8090.
Tokmakov, P., Li, J., Burgard, W., & Gaidon, A. (2021). Learning to Track with Object Permanence. ICCV 2021.
Geiger, A., Lenz, P., & Urtasun, R. (2012). Are We Ready for Autonomous Driving? The KITTI Vision Benchmark Suite. CVPR 2012, pp. 3354-3361.
Iftikhar, S., Zhang, Z., Asim, M., Muthanna, A., Koucheryavy, A., & Abd El-Latif, A. A. (2022). Deep Learning-Based Pedestrian Detection in Autonomous Vehicles: Substantial Issues and Challenges. Electronics, 11(21), 3551.
Notes: Backup slide for Q&A - full reading list behind the project. One caveat for your own awareness: the author list for the first entry (the dual-appearance / DADA-Track paper) came from a secondary search result rather than a directly verified page, since the publisher page blocked direct access - worth a quick manual check against the actual journal listing before you present this, just to be safe. Everything else was verified against the source page or a well-corroborated listing.

## Slide 17
Thank you!
Questions?
Notes: Close with the roadmap: this baseline experiment was step one, the frozen-memory experiment was step two, the SORT test was step three. Next comes fixing the SORT experiment's methodology, building proper test sets, implementing OATM itself, and comparing it fairly against existing tracking methods. Also flag scope: everything so far has been vehicles - pedestrians and other vulnerable road users are the next class to extend to, since that's arguably the higher-stakes case. Open the floor for questions.