## Slide 11
SRSI RESEARCH PROJECT
Occlusion-Adaptive Temporal Memory
Giving self-driving cars short-term memory for hidden objects
Noor Basfar
Notes: This follows straight after your hook - it's the reveal of what the project actually is. Introduce the project over the real dashcam frame: this is about helping self-driving car cameras keep track of road users even when something briefly blocks the view.

## Slide 12
THE PROBLEM IN AUTONOMOUS DRIVING
Single-frame detectors forget what they can't see
BEFORE
Car clearly visible
OCCLUDED
Fully hidden from view
AFTER
Reappears down the road
→
→
A detector that only looks at the middle frame has no idea a car is even there.
“Like watching someone walk behind a parked bus — you don't assume they vanished.”
Notes: Walk through this one real example frame by frame: the car is visible, then fully hidden behind other traffic, then reappears further down the road. Point out that most detectors process the middle frame in total isolation - to them, the car simply doesn't exist for that instant. That's the core problem this whole project is about.

## Slide 13
THE DATASET
nuScenes — Front Camera Only
1
nuScenes: a large-scale AV dataset with synchronized cameras, LiDAR, radar, and 3D box annotations that include a per-object visibility rating
2
This project uses only CAM_FRONT — one monocular camera, no LiDAR or other views feeding detection itself
3
Front-only keeps the pipeline laptop-scale and isolates the occlusion-memory problem, instead of mixing in multi-camera fusion
4
LiDAR and the 3D annotations aren't wasted, though — they come back as independent ground truth for evaluating OATM (next: Evaluation Methodology)
CAM_FRONT — the only view this project detects from
Notes: Be upfront about scope before going further: this is nuScenes, and specifically only the forward-facing camera - no LiDAR, no side/rear cameras, no sensor fusion feeding the detector. That's a deliberate simplification to keep the study laptop-scale and focused purely on the occlusion-memory question. The payoff comes later - nuScenes' LiDAR and 3D annotations aren't part of detection, but they become the independent ground truth used to evaluate OATM, which is the next thing after the design slide.

## Slide 14
THE CORE RESEARCH QUESTION
Can short-term visual memory help a camera keep track of temporarily hidden road users — without inventing false ones?
Hypothesis
Occlusion-aware temporal memory preserves more valid tracks through short occlusions than single-frame detection or conventional tracking — without creating an unacceptable number of false, ghost tracks.
Notes: State the research question plainly and pause on it. This is the question the whole project is trying to answer, and the hypothesis is what we expect but haven't yet proven.

## Slide 15
EVIDENCE 1 · BASELINE
Detection Collapses at Full Occlusion
Pretrained YOLO nano, CPU-only, on 8 real nuScenes occlusion sequences — tracked through 5 stages, from clearly visible to fully hidden and back.
Chart: Detection rate by stage
| No Occlusion | First Partial Occlusion | Full Occlusion | First Partial Appearance | Full Appearance
Detection rate | 1 | 1 | 0.125 | 0.5 | 1
Chart: Mean confidence by stage (0 = undetected)
| No Occlusion | First Partial Occlusion | Full Occlusion | First Partial Appearance | Full Appearance
Mean confidence | 0.774 | 0.587 | 0.029 | 0.425 | 0.845
Full occlusion, sample_003 — YOLO draws zero boxes on the target. Not misdetected — simply absent.
100% → 13%
detection rate at full occlusion
0.77 → 0.03
mean confidence at full occlusion
100%
correct class whenever detected
Partial-occlusion stages have small sample sizes (n=2-3) — interpret with caution.
Notes: Baseline setup: a plain, off-the-shelf YOLO detector, no memory at all. Point at the photo - that's the actual failure, a real frame where the detector produced zero boxes for the hidden target, not a simulated one. Detection rate stays perfect through partial occlusion then falls off a cliff at full occlusion. Confidence erodes before detection technically fails, and recovers once visible again.

## Slide 16
EVIDENCE 2 · NAIVE MEMORY
The Simplest Fix: Freeze the Last Box
When YOLO loses the target, keep drawing its last known box instead of letting it vanish.
BEST CASE
WORST CASE
sample_003 — reappears next to a bus (83 px, IoU 0.34 — boxes barely overlap by a third)
sample_006 — crossing an intersection (589 px, IoU 0.00)
Also tested: sample_001 (127px), sample_004 (423px), sample_005 (432px) — same pattern across all 5.
331 px
mean center error on reappearance
0.085
mean IoU (median: 0.000)
3 / 5
samples had zero box overlap
Notes: Introduce the naive fix: just freeze the last box while the target is hidden. Orange is the frozen memory box, green is the real detection once the object reappears. Best case they nearly line up; worst case the frozen box is nowhere near the real car. Not cherry-picked - all 5 valid samples follow the same pattern, mean error 331px, 3 of 5 with zero overlap at all.

## Slide 17
EVIDENCE 3 · SORT MOTION PREDICTION
Motion Prediction Helps — With Caveats
A mini SORT-style tracker predicting velocity instead of freezing position — tested on 9 real car tracks.
Chart: Center error by gap length (px)
| 1 | 2 | 3 | 5 | 8 | 10
Static memory | 12.778 | 16.152 | 22.286 | 34.21 | 51.616 | 64.485
SORT motion | 3.472 | 3.3 | 4.588 | 6.503 | 14.295 | 31.329
Chart: Mean IoU by gap length
| 1 | 2 | 3 | 5 | 8 | 10
Static memory | 0.887 | 0.86 | 0.817 | 0.737 | 0.628 | 0.575
SORT motion | 0.921 | 0.905 | 0.882 | 0.838 | 0.702 | 0.57
46 → 17 px
mean center error, static → SORT
0.67 → 0.72
mean IoU, static → SORT
9 tracks
cars only, across 3 clips
THE CATCH
Almost the entire win comes from 2 of 9 tracks — on the dominant clip, static memory ties SORT. The reference boxes were Kalman-corrected (not raw YOLO), and long gaps bypass the tracker's own expiry rule. A real demonstration of motion extrapolation — not yet an independent validation of SORT.
Notes: Motion prediction beats a frozen box clearly - 46px down to 17px, IoU up from 0.673 to 0.720. But say the catch out loud: almost the whole win comes from 2 of 9 tracks, the reference boxes aren't fully independent, and long gaps bypass the tracker's own expiry rule. A real result, not yet a fully validated one.

## Slide 18
THE DIAGNOSIS
A static memory box goes stale because it ignores motion.
Real objects keep moving while hidden. A memory system that only remembers where something was will drift further wrong the longer it stays hidden.
THE GAP IN EXISTING TOOLS
Single-frame detection
no memory at all — occluded means gone
SORT
cuts error 46→17px on smooth tracks — but N=9 cars, circular reference
ByteTrack
still needs some visible evidence to link to
Fixed temporal memory
blind to motion and its own ghost-track risk
None decide hidden vs. lost vs. gone, or decay confidence accordingly — that's the gap OATM is built to fill.
Notes: This is the pivot of the whole talk. First state the diagnosis: naive memory fails because it ignores motion, and even real motion prediction (as just shown) only helps partially. Then name the gap in every existing lightweight method - none of them combine occlusion-causality reasoning, motion prediction, and confidence decay. That's the bridge into the OATM design on the next slide.

## Slide 19
THE PROPOSED FIX
OATM: Occlusion-Adaptive Temporal Memory
1
Appearance memory: stores the last clear crop of the object, so it can be re-identified on reappearance
2
Motion memory: a Kalman-style predict → observe → correct loop — the same mechanism already prototyped in Evidence 3, fixed to use an independent reference and real track-expiry
3
Occlusion classifier: VISIBLE / OCCLUDED / LOST / EXITED — decides how much to trust the motion prediction right now
4
Confidence decays smoothly, not on a fixed countdown; anti-ghost termination retires a track before it becomes a phantom
VISIBLE
OCCLUDED
LOST / EXITED
reappearance → back to VISIBLE
Notes: Introduce OATM's core mechanism, and be specific about the motion half since that's the part judges will probe: it's not a vague promise, it's the same predict-observe-correct Kalman loop already built and tested in Evidence 3 - just corrected to use an independent reference box and to actually enforce track-expiry, the two flaws that experiment exposed. Appearance memory (last clear crop) handles re-identification; motion memory (position + velocity) handles where to look. The occlusion classifier decides how much to trust the motion prediction at any moment, and confidence decays smoothly rather than on a fixed timer. Be clear this is the proposed design - it has not been implemented or benchmarked yet, that's the next phase.

## Slide 20
EVALUATION METHODOLOGY
Ground Truth From LiDAR, Not the Camera Itself
1
Use nuScenes' 3D box annotations + LiDAR point cloud as ground truth, projected into CAM_FRONT — never derived from the front camera's own detections
2
Run OATM exactly as designed: CAM_FRONT only, genuinely blind to the object during its occluded frames
3
Score OATM's predicted position during occlusion against that projected LiDAR / 3D ground truth, not against another camera-based tracker
4
This directly fixes the circularity in Evidence 3, where the reference boxes came from the same Kalman model being tested
The front camera can't see through the occlusion — but LiDAR still can. That's what makes this an independent check.
Notes: This is the answer to 'how will you actually know OATM is right.' The key move: ground truth comes from LiDAR and the 3D box annotations, not from another camera-derived tracker - so it isn't circular the way the SORT experiment's evaluation was. The front camera is blind during occlusion by design; LiDAR isn't, so it gives an independent check on whether OATM's predicted position is actually correct, not just self-consistent.

## Slide 21
HOW OATM COMPARES
A Design Comparison
OATM has not been implemented or measured yet — this is a design-level comparison.
Method | How it works | Main weakness
Single-frame detection | Looks only at the current image | Hidden object instantly disappears
SORT | Predicts motion — measured 46 → 17px error on 9 tracks | Tiny sample; reference partly circular; expiry bypassed
ByteTrack | Links strong and weak detections | Still needs some visible evidence
Fixed temporal memory | Keeps missing objects for N frames | May forget early or keep ghosts too long
OATM (proposed) | Appearance + motion + occlusion-aware decay | More complex; needs careful tuning
Notes: Position OATM against the alternatives already used in the field. The point isn't that the others are bad - it's that none of them explicitly reason about *why* an object disappeared, which is what OATM adds. Reiterate that this row is a design claim to be tested, not a measured result.

## Slide 23
ROADMAP
Proving It
1
Build natural + controlled occlusion test sets from nuScenes
2
Fix SORT's circular reference and disabled track-expiry, add ByteTrack, then benchmark all 5 against OATM
3
Metrics: occluded-object recall, identity preservation, ghost-track rate, recovery time
4
Split train / validation / test by scene, not by frame, to avoid leakage
5
Expand from vehicle-only tracking to pedestrians and other vulnerable road users
Notes: Close with the roadmap: this baseline experiment was step one, the frozen-memory experiment was step two, the SORT test was step three. Next comes fixing the SORT experiment's methodology, building proper test sets, implementing OATM itself, and comparing it fairly against existing tracking methods. Also flag scope: everything so far has been vehicles - pedestrians and other vulnerable road users are the next class to extend to, since that's arguably the higher-stakes case. Open the floor for questions.

## Slide 24
References
Ma, J., Yang, J., Fu, F., Hao, D., & Wang, R. (2026). Occlusion-aware multi-camera 3D multi-object tracking with dual-appearance dynamic association. Applied Soft Computing.
Pang, Z., Li, J., Tokmakov, P., Chen, D., Zagoruyko, S., & Wang, Y.-X. (2023). Standing Between Past and Future: Spatio-Temporal Modeling for Multi-Camera 3D Multi-Object Tracking. CVPR 2023. arXiv:2302.03802.
Anwar, N., Bilodeau, G.-A., & Bouachir, W. (2024). STF: Spatio-Temporal Fusion Module for Improving Video Object Detection. arXiv:2402.10752.
Cai, J., Xu, M., Li, W., Xiong, Y., Xia, W., Tu, Z., & Soatto, S. (2022). MeMOT: Multi-Object Tracking with Memory. CVPR 2022, pp. 8080-8090.
Tokmakov, P., Li, J., Burgard, W., & Gaidon, A. (2021). Learning to Track with Object Permanence. ICCV 2021.
Geiger, A., Lenz, P., & Urtasun, R. (2012). Are We Ready for Autonomous Driving? The KITTI Vision Benchmark Suite. CVPR 2012, pp. 3354-3361.
Iftikhar, S., Zhang, Z., Asim, M., Muthanna, A., Koucheryavy, A., & Abd El-Latif, A. A. (2022). Deep Learning-Based Pedestrian Detection in Autonomous Vehicles: Substantial Issues and Challenges. Electronics, 11(21), 3551.
Notes: Backup slide for Q&A - full reading list behind the project. One caveat for your own awareness: the author list for the first entry (the dual-appearance / DADA-Track paper) came from a secondary search result rather than a directly verified page, since the publisher page blocked direct access - worth a quick manual check against the actual journal listing before you present this, just to be safe. Everything else was verified against the source page or a well-corroborated listing.

## Slide 25
Thank you!
Questions?
(pls say no)
Notes: Close with the roadmap: this baseline experiment was step one, the frozen-memory experiment was step two, the SORT test was step three. Next comes fixing the SORT experiment's methodology, building proper test sets, implementing OATM itself, and comparing it fairly against existing tracking methods. Also flag scope: everything so far has been vehicles - pedestrians and other vulnerable road users are the next class to extend to, since that's arguably the higher-stakes case. Open the floor for questions.