## Slide 1
SRSI RESEARCH PROJECT — FINAL METHOD
Occlusion-Adaptive Temporal Memory
Camera-Only Object Persistence Through Temporary Occlusion
Noor Basfar
Notes: This is the updated, implemented method - not a design proposal anymore. OATM now means relational target-occluder memory, and it has been built and evaluated against two ByteTrack baselines on nuScenes mini. Everything in this deck traces to run lidar-fixes-20260805.

## Slide 2
THE PROBLEM
Cameras Lose Track of Things They Cannot See
A camera only ever looks at the frame in front of it. When one vehicle drives behind another, the detector can miss it completely — and when it comes back into view, treat it as a brand-new vehicle it has never seen before.
The car never went anywhere. Only the camera's view of it did — and that is the difference the tracker has to work out on its own.
“Like watching someone walk behind a parked bus — you don't assume they vanished.”
2
→
→
Target vehicle
Target hidden behind occluder
Target vehicle (reappeared)
BEFORE
OCCLUDED
AFTER
Car clearly visible
Fully hidden from view
Reappears down the road
Notes: Anchor the whole talk on this one real sequence. Point at the boxes: the green car is what we want to follow, the orange truck is what hides it, and the dashed box is where the car actually is while the camera cannot see it. The car never disappeared - only the view of it did. That distinction is the entire project.

## Slide 3
THE DATASET
nuScenes — Front Camera Only
1
nuScenes-mini: a large-scale autonomous-driving dataset with synchronized cameras, LiDAR, radar, and 3D box annotations across 10 scenes.
2
OATM's tracker uses only CAM_FRONT — one monocular camera feed, split five scenes for development and five held out for validation.
3
2,342 causal camera frames were processed online; 404 official annotated keyframes were scored, covering 3,492 in-scope car and pedestrian annotations.
4
LiDAR and the 3D annotations aren't wasted, though — they return later as independent offline ground truth, never as input to the tracker itself.
CAM_FRONT — the only view OATM detects from
nuScenes sensor pipeline
Camera + LiDAR + Radar
→
CAM_FRONT selected
→
Detection input (yolo26n.pt)
3
Notes: Same dataset scope as the earlier assignment work: nuScenes-mini, CAM_FRONT only, online. LiDAR and 3D annotations only ever come back offline, during evaluation - that boundary is explained explicitly two slides from now.

## Slide 4
THE RESEARCH QUESTION
Can temporal video understanding enable a camera to maintain reliable tracks of temporarily occluded road users, without introducing false detections?
Hypothesis
A tracker should keep following a hidden object only while something visible actually explains why it disappeared. Working out where the object went from the thing blocking it should find more of them again — while inventing fewer that were never there — than giving every lost object the same fixed waiting time.
4
Notes: State the question plainly. The hypothesis is specific: persistence should be *conditional* on evidence, not a fixed timer applied to every missing object equally.

## Slide 5
METHODOLOGY
Marking Each Stage of the Occlusion Manually
No automated tool identifies the precise moment an object becomes occluded or reappears. Each occlusion sequence in this study was therefore manually reviewed, frame by frame, and divided into five stages before any detector was run.
This manual staging is what makes the stage-by-stage detection results on the next slide meaningful — each stage boundary reflects a human judgment, not an automatic threshold.
1. No Occlusion
Target fully visible
→
2. First Partial
Occluder begins covering
→
3. Full Occlusion
Target entirely blocked
→
4. First Reappearance
Target partially visible
→
5. Full Appearance
Target fully visible again
5

## Slide 6
STEP 1 · THE DETECTOR ALONE
Detection Performance Across Occlusion Stages
Pretrained YOLO nano, CPU-only, on 8 real nuScenes occlusion sequences — tracked through 5 stages, from clearly visible to fully hidden and back.
Chart: Detection rate by stage
| No Occlusion | First Partial Occlusion | Full Occlusion | First Partial Appearance | Full Appearance
Detection rate | 1 | 1 | 0.125 | 0.5 | 1
Chart: Mean confidence by stage (0 = undetected)
| No Occlusion | First Partial Occlusion | Full Occlusion | First Partial Appearance | Full Appearance
Mean confidence | 0.774 | 0.587 | 0.029 | 0.425 | 0.845
Full occlusion, sample_003: the detector produces no bounding box for the target. This reflects a missed detection, not a misclassification.
100% → 13%
detection rate at full occlusion
0.77 → 0.03
mean confidence at full occlusion
100%
correct class whenever detected
Partial-occlusion stages have small sample sizes (n=2-3) — interpret with caution.
6
Notes: Baseline setup: a plain, off-the-shelf YOLO detector, no memory at all. Point at the photo - that's the actual failure, a real frame where the detector produced zero boxes for the hidden target, not a simulated one. Detection rate stays perfect through partial occlusion then falls off a cliff at full occlusion. Confidence erodes before detection technically fails, and recovers once visible again.

## Slide 7
STEP 2 · REMEMBERING THE LAST BOX
Baseline Approach: Keep Showing Where It Used to Be
When the detector loses the car, we simply keep drawing the last box it saw instead of dropping it. The car keeps moving; the box does not.
BEST CASE
WORST CASE
sample_003 — reappears next to a bus (83 px, IoU 0.34 — boxes barely overlap by a third)
sample_006 — crossing an intersection (589 px, IoU 0.00)
Also tested: sample_001 (127px), sample_004 (423px), sample_005 (432px) — same pattern across all 5.
331 px
mean center error on reappearance
0.085
mean IoU (median: 0.000)
3 / 5
samples had zero box overlap
7
Notes: Introduce the naive fix: just freeze the last box while the target is hidden. Orange is the frozen memory box, green is the real detection once the object reappears. Best case they nearly line up; worst case the frozen box is nowhere near the real car. Not cherry-picked - all 5 valid samples follow the same pattern, mean error 331px, 3 of 5 with zero overlap at all.

## Slide 8
STEP 2 · REMEMBERING THE LAST BOX
Watching That Idea Fail, Side by Side
Four views of the same sequence, shown side by side: the detector alone (track lost), static memory's retained position, motion-based prediction, and the withheld reference used to evaluate accuracy. The static-memory panel drifts away from the vehicle as it continues moving.
.
8

## Slide 9
STEP 3 · PREDICTING MOVEMENT
Second Try: Guess Where It Is Heading: SORT
Instead of freezing the last box, this version works out how fast the car was moving and carries it forward while it is out of sight. Tested on 9 vehicles.
Chart: Center error by gap length (px)
| 1 | 2 | 3 | 5 | 8 | 10
Static memory | 12.778 | 16.152 | 22.286 | 34.21 | 51.616 | 64.485
SORT motion | 3.472 | 3.3 | 4.588 | 6.503 | 14.295 | 31.329
Chart: Mean IoU by gap length
| 1 | 2 | 3 | 5 | 8 | 10
Static memory | 0.887 | 0.86 | 0.817 | 0.737 | 0.628 | 0.575
SORT motion | 0.921 | 0.905 | 0.882 | 0.838 | 0.702 | 0.57
46 → 17 px
mean center error, static → SORT
0.67 → 0.72
mean IoU, static → SORT
9 tracks
cars only, across 3 clips
THE CATCH
Most of the improvement is concentrated in 2 of the 9 tracks; on the dominant clip, static memory performs comparably to SORT. The reference boxes used for evaluation were Kalman-corrected rather than raw YOLO detections, and gaps exceeding the tracker's configured expiry threshold were not enforced. This demonstrates motion extrapolation under controlled conditions, not an independent validation of SORT.
9
Notes: Motion prediction beats a frozen box clearly - 46px down to 17px, IoU up from 0.673 to 0.720. But say the catch out loud: almost the whole win comes from 2 of 9 tracks, the reference boxes aren't fully independent, and long gaps bypass the tracker's own expiry rule. A real result, not yet a fully validated one.

## Slide 10
STEP 4 · USING WEAK DETECTIONS
Third Try: Do Not Throw Away Faint Sightings: ByteTrack
Same test as the previous step. This time, faint detections the detector was unsure about are reused rather than thrown away — measured on 12 real weak-sighting events and 65 frames where the car was not detected at all.
58% → 67%
natural events recovered (SORT → ByteTrack)
33% → 50%
identity preserved through the event
2 → 0
false associations during complete detection absence
THE CATCH
The improvement is concentrated in the pedestrian class (2 of 4 events) and is drawn from only 5 target tracks across 4 scenes. It also applies only when a weak detection still exists; when the object is entirely undetected, ByteTrack relies on the same motion prediction as SORT.
This illustrates the distinction OATM's occlusion classifier is intended to model: weak-but-present evidence, where a secondary association step is beneficial, versus truly absent evidence, where only motion and uncertainty modeling can contribute.
10

## Slide 11
STEP 5 · THE DIAGNOSIS
Why None of These Are Enough
Real objects continue moving while hidden. A memory system that retains only a past position becomes increasingly inaccurate the longer the object remains occluded.
THE GAP IN EXISTING TOOLS
Single-frame detection
Retains no information across frames; an occluded object is treated as absent
SORT
Reduces center error from 46 to 17 px on smooth trajectories; evaluated on 9 vehicle tracks with a circular reference
ByteTrack
Requires at least partial detection evidence to associate a track
Fixed temporal memory
Does not model motion and risks retaining tracks after the object has left the scene
None of these methods distinguish between an occluded, lost, or exited object, or adjust confidence accordingly — this is the gap OATM is designed to address.
11
Notes: This is the pivot of the whole talk. First state the diagnosis: naive memory fails because it ignores motion, and even real motion prediction (as just shown) only helps partially. Then name the gap in every existing lightweight method - none of them combine occlusion-causality reasoning, motion prediction, and confidence decay. That's the bridge into the OATM design on the next slide.

## Slide 12
WHAT MAKES OATM DIFFERENT
Four Ideas Standard Tracking Does Not Have
1
It looks for what is blocking
A hidden object is only kept alive if something visible could genuinely be hiding it — it is never granted automatically.
target–occluder relational memory
2
It works out where the object went
The hidden position is read off the blocking vehicle's movement, and only believed if a separate motion estimate agrees with it.
occluder-centric geometry with motion consistency
3
It knows when to stop waiting
OATM predicts when the object should come back into view, and drops the track cleanly if it does not appear.
expected clearance and uncertainty termination
4
It protects the identity
A stricter re-matching check stops the track from latching onto the wrong vehicle when it reappears.
protected reappearance stage
12
Notes: Four ideas, and the bold line on each card is the one to say out loud - the small italic line underneath is the formal name if an examiner wants it. The thread through all four: OATM never guesses forever. Every part of it has a stopping condition tied to something the camera can actually see.

## Slide 13
HOW IT WORKS
What OATM Does, Step by Step
Relational OATM activates only for an established track that goes unmatched — every other detection follows ordinary ByteTrack association.
13
Notes: This is the real pipeline diagram from the implementation, not a mockup. Walk left to right: detections, standard ByteTrack rounds, then - only for a mature target that's still unmatched - camera-motion estimation, the target-occluder relation graph, clearance prediction, and finally a protected reappearance stage that decides whether to restore the identity or terminate it. Every box before 'Output' is invisible to the final saved result unless the target was genuinely unmatched.

## Slide 14
SEEING IT WORK
OATM Holding On to a Car It Cannot See
The real tracker, running on camera frames only. A black SUV moves across the car being followed; the detector stops seeing it, but OATM keeps the identity alive and carries the box forward until it comes back.
Scene fcbccedd, frames 68-142. Green = detected this frame · orange = the vehicle OATM blamed for the occlusion · dashed blue = held from memory, with no detection at all. Plays automatically in slideshow.

## Slide 15
CHECKING THE ANSWERS
Marking OATM Against LiDAR, Not Against Itself
LiDAR provides positional information independent of the camera, allowing OATM's predictions to be evaluated even when the target is not visible to the camera.
3D + LiDAR Ground Truth
nuScenes annotations, independent of camera
→
Project to CAM_FRONT
Standard transform chain into the camera view
→
Run OATM (Blind)
CAM_FRONT only, genuinely occluded
→
Score vs. Ground Truth
Never against another camera-based tracker
This ordering fixes the circular test in Step 3, where the answers being marked against came from the very same motion model being tested.
14
Notes: This is the answer to 'how will you actually know OATM is right.' The key move: ground truth comes from LiDAR and the 3D box annotations, not from another camera-derived tracker - so it isn't circular the way the SORT experiment's evaluation was. The front camera is blind during occlusion by design; LiDAR isn't, so it gives an independent check on whether OATM's predicted position is actually correct, not just self-consistent.

## Slide 16
KEEPING THE TEST FAIR
What OATM Sees, and What Only the Marking Sees
Online, the tracker only ever sees CAM_FRONT frames and its own history. Offline, after the tracker has already saved its output, the evaluator brings in projected ground truth to grade it — with no feedback path back to the tracker.
LiDAR point count is not an occlusion classifier. The most-occluded evaluation bin comes from nuScenes visibility token 1 (0–40% visible), never from LiDAR alone.
15
Notes: This is the answer to 'how do you know OATM is right, and isn't LiDAR cheating.' Two completely separate worlds: online, the tracker only ever sees camera frames and its own history. Offline, after the tracker has already saved its output, the evaluator brings in projected 3D annotations and visibility labels to grade it - by class-aware Hungarian matching at IoU 0.30 - and only then computes precision, F1, MOTA, IDF1, and localization error. No feedback ever flows back into the tracker.

## Slide 17
THE RESULTS
How OATM Did Against ByteTrack
All three methods were given exactly the same detections, so any difference comes from the tracking alone. 10 scenes, 1,873 checked objects — run lidar-fixes-20260805.
Method | Precision | F1 | MOTA | IDF1 | ID switches | Center error
ByteTrack-5 | 73.4% | 40.1% | 14.2% | 29.6% | 64 | 21.084 px
ByteTrack-12 | 55.3% | 37.7% | 1.1% | 27.4% | 82 | 21.361 px
OATM | 84.1% | 40.4% | 18.4% | 30.3% | 59 | 20.055 px
39.4%
predicted-hidden precision (vs. 25.0% / 14.0%)
7.8%
unsupported-track rate (vs. 25.9% / 22.1%)
28
fragmentations — fewest of all three methods
17
Notes: This is the headline slide. OATM wins on precision, F1, MOTA, IDF1, identity switches, and localization - all on identical input detections. The stat ribbon covers the two numbers that matter most for the 'why not just increase the buffer' question: OATM is far more precise about when it's genuinely still tracking a hidden object, not just waiting longer.

## Slide 18
SENSOR CHOICES
What Each Sensor Setup Can and Cannot Do
A generic comparison of sensor configurations used in autonomous vehicle perception. OATM's own row now reflects an implemented tracking method with a real, final nuScenes-mini validation result (see Results); the sensor-modality comparison itself remains a conceptual framing.
Configuration | Description | Video Understanding Capability
Single camera | One forward-facing monocular camera | No temporal reasoning by default — each frame is processed independently
LiDAR only | 360-degree point cloud, no camera imagery | Tracks geometry continuously, but has no visual or semantic content to reason with
Multi-camera (5-6 cameras) | Full surround visual coverage | Wider visual context, but each stream is still typically processed frame by frame
Camera + LiDAR fusion | Combines visual and geometric sensing | Richer combined signal, but reasoning over that signal across time is a separate, unsolved problem
Single camera + OATM (proposed) | Same low-cost hardware, with temporal occlusion reasoning added | Adds explicit target-occluder relational reasoning, occluder-centric memory, and expected-clearance termination across frames
16
Notes: This slide is about hardware/modality trade-offs, not tracking methods -- keep that framing. The one thing to update out loud: OATM's own row used to say 'not yet implemented or measured'; it no longer is. OATM has now been evaluated as a tracking method on a final scene-disjoint nuScenes-mini validation (ten scenes, five held out, 1,873 annotations, run lidar-fixes-20260805) -- see the Results slide next. The sensor-configuration comparison itself is still conceptual -- this slide is about which hardware you'd deploy it on, not whether the method itself works.

## Slide 19
IN SUMMARY
Results and Conclusion
84.1%
of the objects OATM reported
were really there
ByteTrack: 73.4% and 55.3%
59
identity mix-ups —
the fewest of the three
ByteTrack: 64 and 82
7.8%
of its hidden guesses were
unsupported by anything real
ByteTrack: 25.9% and 22.1%
OATM held on to hidden objects more carefully than simply waiting longer — better on accuracy, identity and position, all from the same detections.
Where it still loses: it found slightly fewer objects overall (26.6% vs 27.6% and 28.6%), and fewer again when they were almost completely hidden. That is the next thing to fix.
A better trade-off than a fixed waiting time on this ten-scene study — not a claim that it wins everywhere.
18
Notes: Three numbers, then what they mean together, then the honest limit - in that order. The 7.8% is the one to dwell on: it is the answer to 'why not just wait longer', because waiting longer is exactly what pushes that number up to 25.9%. Name the recall gap yourself before anyone asks, and close on the scoped claim.

## Slide 20
References
Caesar, H., Bankiti, V., Lang, A. H., Vora, S., Liong, V. E., Xu, Q., Krishnan, A., Pan, Y., Baldan, G., & Beijbom, O. (2020). nuScenes: A multimodal dataset for autonomous driving. CVPR 2020, 11618-11628.
Bewley, A., Ge, Z., Ott, L., Ramos, F., & Upcroft, B. (2016). Simple online and realtime tracking. 2016 IEEE ICIP, 3464-3468.
Zhang, Y., Sun, P., Jiang, Y., Yu, D., Weng, F., Yuan, Z., Luo, P., Liu, W., & Wang, X. (2022). ByteTrack: Multi-object tracking by associating every detection box. ECCV 2022.
Cai, J., Xu, M., Li, W., Xiong, Y., Xia, W., Tu, Z., & Soatto, S. (2022). MeMOT: Multi-Object Tracking with Memory. CVPR 2022, pp. 8080-8090.
Tokmakov, P., Li, J., Burgard, W., & Gaidon, A. (2021). Learning to Track with Object Permanence. ICCV 2021.
Zhu, X., Wang, Y., Dai, J., Yuan, L., & Wei, Y. (2017). Flow-Guided Feature Aggregation for Video Object Detection. ICCV 2017, 408-417.
Gao, R., & Wang, L. (2023). MeMOTR: Long-Term Memory-Augmented Transformer for Multi-Object Tracking. ICCV 2023, pp. 9901-9910.
19
Notes: nuScenes is cited first because every number in this deck is measured on it. SORT and ByteTrack are the two methods OATM is built on and compared against. The remaining four are the memory and object-permanence line of work that motivates the gap OATM targets.

## Slide 21
Thank you!
Questions?
Notes: Good questions to have ready: why not just raise ByteTrack's buffer (answer: 393 false predicted-hidden matches at buffer 12, vs OATM's 40), whether this is still camera-only if nuScenes LiDAR was used anywhere (answer: offline evaluation only, never online), and the severe-visibility recall gap (honest weakest point, named directly in Limitations).