## Slide 1
👁
Occlusion-Adaptive Temporal Memory
Giving self-driving cars short-term memory for hidden objects
An nuScenes-based autonomous-vehicle perception research project
Notes: Introduce the project: this is about helping self-driving car cameras keep track of road users even when something briefly blocks the view. Set up that this is an active research project, not just a class exercise.

## Slide 2
Single-frame detectors forget what they can't see
• Most object detectors look at one camera image at a time
• If a truck briefly blocks a pedestrian, the model treats them as gone
• When the pedestrian reappears, it's logged as a brand-new person, not the same one
❓
“Imagine watching someone walk behind a parked bus — you don't assume they vanished.”
Notes: Explain the core problem with a simple analogy. Point to the callout: humans naturally remember what was there a moment ago; most detectors don't. That's the gap this project is trying to close.

## Slide 3
THE CORE RESEARCH QUESTION
Can short-term visual memory help a camera keep track of temporarily hidden road users — without inventing false ones?
Hypothesis: occlusion-aware temporal memory preserves more valid tracks through short occlusions than single-frame detection or conventional tracking — without creating an unacceptable number of false, ghost tracks.
Notes: State the research question plainly and pause on it. This is the question the whole project is trying to answer, and the hypothesis is what we expect but haven't yet proven.

## Slide 4
Step One: Measuring the Baseline
📷
Dataset: nuScenes CAM_FRONT — 8 real occlusion sequences
🧠
Model: pretrained YOLO nano (yolo26n) — prediction only, no training
🖥
CPU only, image size 640, confidence threshold 0.05
🔁
5 stages per object: before → first partial occlusion → full occlusion → first reappearance → full appearance
Real YOLO detections on a nuScenes frame
Notes: Walk through the method: we didn't build anything fancy yet, just measured how a plain, off-the-shelf detector behaves as an object goes through five occlusion stages. Point out the real annotated example image.

## Slide 5
Detection Collapses at Full Occlusion
Chart: Detection rate by stage
| No Occlusion | First Partial Occlusion | Full Occlusion | First Partial Appearance | Full Appearance
Detection rate | 1 | 1 | 0.125 | 0.5 | 1
Chart: Mean confidence by stage (0 = undetected)
| No Occlusion | First Partial Occlusion | Full Occlusion | First Partial Appearance | Full Appearance
Mean confidence | 0.774 | 0.587 | 0.029 | 0.425 | 0.845
Partial-occlusion and first-reappearance stages have small sample sizes (n=2-3) — interpret with caution.
Notes: Show the two charts together. Detection rate stays perfect through partial occlusion then falls off a cliff at full occlusion. Confidence tells a smoother story: it erodes before detection technically fails, and recovers once the object is visible again.

## Slide 6
What We Learned
100% → 12%
detection rate at full occlusion
0.77 → 0.03
mean confidence at full occlusion
100%
correct class whenever something was detected
The detector doesn't fade out gradually — it's either fully seen or fully gone. That gap is exactly what temporal memory can fill.
Notes: Summarize the three headline numbers. The key insight: confidence decays smoothly but detection itself is almost binary. That binary drop is the opportunity for a memory-based system to smooth over.

## Slide 7
The Proposed Fix: OATM
Occlusion-Adaptive Temporal Memory
🧩
Dual memory: appearance (last clear view) + motion (position & velocity)
🚦
Occlusion classifier: VISIBLE / OCCLUDED / LOST / EXITED
⏳
Confidence decays smoothly over time — not a fixed countdown
🚫
Anti-ghost termination stops phantom tracks from lingering
VISIBLE
OCCLUDED
LOST / EXITED
reappearance → back to VISIBLE
Notes: Introduce OATM's core mechanism: it doesn't just keep every missing object alive, it explicitly classifies whether something is occluded, lost, or has exited frame, and decays confidence smoothly rather than on a fixed timer.

## Slide 8
How OATM Compares
Method | How it works | Main weakness
Single-frame detection | Looks only at the current image | Hidden object instantly disappears
SORT | Predicts motion from recent pattern | Struggles with turns or ego-motion
ByteTrack | Links strong and weak detections | Still needs some visible evidence
Fixed temporal memory | Keeps missing objects for N frames | May forget early or keep ghosts too long
OATM (proposed) | Appearance + motion + occlusion-aware decay | More complex; needs careful tuning
Notes: Position OATM against the alternatives already used in the field. The point isn't that the others are bad — it's that none of them explicitly reason about *why* an object disappeared, which is what OATM adds.

## Slide 9
What's Next
🧪
Build natural + controlled occlusion test sets from nuScenes
📊
Compare 5 systems: single-frame, SORT, ByteTrack, fixed memory, OATM
📏
Metrics: occluded-object recall, identity preservation, ghost-track rate, recovery time
🎬
Split train / validation / test by scene, not by frame, to avoid leakage
Thank you — questions welcome
Notes: Close with the roadmap: this baseline experiment was step one. Next comes building proper test sets, implementing OATM itself, and comparing it fairly against existing tracking methods using metrics that specifically capture occlusion handling and false-track risk.